## Slide 1
RUL LAB
01
01
PREDICTIVE MAINTENANCE / PHASE 1
Remaining Useful Life
Prediction for Industrial Engines
Machine-learning baseline on engineered degradation features
NASA C-MAPSS / SUBSET FD001
TEAM: Kush Puri, Aadit Vachher, Kushagra Maheshwari, Vachan Gupta, Aabir Sarkar • COURSE: CSAI
PHASE 1 / C-MAPSS FD001
01
Notes: Introduce the team and the one-line goal: predict how many cycles an engine has left before it fails.
1

## Slide 2
RUL LAB
01 / THE TARGET
How much life
remains?
Regression target: operating cycles left before failure.
Sensors drift as components wear. Failure is not always sudden.
Phase 1 asks how far engineered features + classical ML can go.
01
Predict from sensor history available up to cycle t
02
Schedule maintenance before failure
03
Avoid replacing parts too early
RUL = last cycle − current cycle
CONCEPTUAL ENGINE LIFETIME
Sensor history → remaining life
OPERATING CYCLE
RUL
cycle t
RUL at t
Every training engine ends at RUL = 0
PHASE 1 / C-MAPSS FD001
02
Notes: Explain RUL in plain words. Regression, not classification. Mention cost of early vs late maintenance.
2

## Slide 3
RUL LAB
02 / DATASET
NASA C-MAPSS
FD001
A controlled simulated benchmark for run-to-failure prediction.
Train rows
20,631
Test rows
13,096
One row = one engine at one cycle
Training engines run to failure. Test engines stop early; ground truth is supplied only at each test engine’s last observed cycle.
100
TRAIN ENGINES
100
TEST ENGINES
21 + 3
SENSORS / CYCLE
+ OP SETTINGS
1 / 1
CONDITION / FAULT MODE
LIFETIME RANGE
~130–360 cycles
FD001: one operating condition, one fault mode
PHASE 1 / C-MAPSS FD001
Source: NASA PCoE C-MAPSS
03
Notes: Train engines run to failure so we can compute true RUL for each row. Test engines stop early; RUL_FD001.txt gives RUL at their last cycle. FD002-4 add operating conditions and fault modes; we start with the simplest as the brief recommends.
3

## Slide 4
RUL LAB
03 / DATA UNDERSTANDING
Data quality &
exploratory analysis
Train-only filtering; visual patterns guide the baseline.
QUALITY CHECKS
01
Missing values: 0
02
Duplicate rows: 0
03
Duplicate pairs: 0
04
Cycle continuity: passed
SENSOR FILTER
Drop std < 0.01: s1, s5, s6, s10, s16, s18, s19
14 sensors retained • no labels used
LIFETIME RANGE
~130–360 cycles
RUL MIX
Most rows: high RUL • minority below 50
SCHEMATIC • NOT A MEASURED HISTOGRAM
SENSOR SIGNAL
Quality checks passed on train and test: 0 missing values, 0 duplicate rows, 0 duplicate engine–cycle pairs, and continuous cycles in both splits.
PHASE 1 / C-MAPSS FD001
04
Notes: Paste the lifetime histogram, RUL histogram and sensor-vs-RUL plots from the notebook here or on backup slides. State what each plot shows in one sentence.
4

## Slide 5
RUL LAB
04 / FEATURE ENGINEERING
57 features.
No future leakage.
At cycle t, every feature uses only same-engine history through t.
Rolling mean
Average of the last 5 cycles; smooths measurement noise.
Rolling slope
(value now − value 4 cycles ago) / 4; captures speed of drift.
Health vs. start
Reading minus that engine’s mean over its first 10 cycles.
FEATURE COUNT
1 cycle + 14 sensors + (14 × 3) = 57
CAUSALITY RULE
Health is 0 before cycle 10 (no future data). No information crosses engines; FD001 needs no regime feature.
PHASE 1 / C-MAPSS FD001
05
Notes: Why each feature: mean removes noise, slope captures speed of drift, health captures distance from the engine's own healthy start. Health is 0 before cycle 10 so early rows never use future data. 57 = 1 cycle + 14 sensors + 14 x 3.
5

## Slide 6
RUL LAB
05 / EVALUATION DESIGN
Split by engine,
never by row
GroupKFold keeps all cycles from one engine in one fold.
Near-duplicate cycles from one engine must not cross train and validation; that would inflate scores.
RMSE
squared-error sensitive
MAE
absolute error
Early MAE
RUL ≥ 50
Late MAE
RUL < 50
ONE ROUND / 5-FOLD GROUPKFOLD
01
20
engines
VALIDATE
02
20
engines
TRAIN
03
20
engines
TRAIN
04
20
engines
TRAIN
05
20
engines
TRAIN
20 held out + 80 train
Repeat until each engine is held out once.
All metrics are in cycles. Final models train on all 100 engines; test once at the final observed cycle. Report CV mean ± std.
PHASE 1 / C-MAPSS FD001
06
Notes: Rows from one engine are highly correlated; a row split puts near-duplicates in train and validation and inflates scores. GroupKFold keeps each engine in one fold. Test set is touched once at the end.
6

## Slide 7
RUL LAB
06 / BASELINES
Three models.
Same test rules.
Model settings are fixed, not tuned; naive defines the floor.
01
Naive baseline
Predicts the training-fold mean RUL. Every useful model should beat this.
BASELINE
02
Elastic Net
Linear reference with L1 + L2 penalty. Scaling stays inside the pipeline. α = 1.0; l1_ratio = 0.5.
LINEAR
03
Random Forest
200 trees; min_samples_leaf = 5. Bootstrap aggregation captures non-linear effects.
NONLINEAR
PHASE 1 / C-MAPSS FD001
07
Notes: Naive sets the floor. Elastic Net is the linear reference (scaling inside the pipeline to avoid leakage). Random Forest averages bootstrapped trees and handles non-linear interactions. Settings were fixed, not tuned.
7

## Slide 8
RUL LAB
07 / RESULTS
Cross-validation
& test results
Five-fold GroupKFold CV is shown as mean ± SD; final test scores use 100 held-out engines.
All error metrics are in cycles. CV and test results are reported separately.
MODEL
DATA
RMSE
MAE
MAE EARLY
MAE LATE
Naive
CV (5 folds)
68.87 ± 1.32
56.86 ± 0.51
48.40 ± 0.71
83.31 ± 0.12
Naive
Test (100)
52.62
40.88
21.44
86.24
Elastic Net
CV (5 folds)
40.04 ± 2.98
30.63 ± 1.56
32.96 ± 2.19
23.35 ± 1.21
Elastic Net
Test (100)
27.98
23.68
25.02
20.55
Random Forest
CV (5 folds)
34.78 ± 1.97
22.79 ± 0.91
28.47 ± 1.11
5.04 ± 0.34
Random Forest
Test (100)
23.34
15.58
20.54
4.02
REPORTING STANDARD
CV mean
± std
Score in cycles
RMSE • MAE
Early MAE: RUL ≥ 50
Late MAE: RUL < 50
CV + TEST
100 test engines
last observed cycle only
Source: notebook Sections 12, 15 and 16 • CV = mean ± SD
PHASE 1 / C-MAPSS FD001
08
Notes: FILL FROM NOTEBOOK Section 16 before presenting. Do not present the numbers until they are copied from your own run.
8

## Slide 9
RUL LAB
08 / ERROR ANALYSIS
Where does the
model fail?
Random Forest cross-validation: early-life errors are larger than late-life errors.
EARLY LIFE
RUL ≥ 50
Healthy-looking engines can have very different remaining lives.
MAE
28.47 ± 1.11
LATE LIFE
RUL < 50
Sensor drift may become clearer as failure approaches.
MAE
5.04 ± 0.34
EARLY / LATE MAE · CV MEAN
28.47
5.04
EARLY · RUL ≥ 50
LATE · RUL < 50
PREDICTED VS TRUE RUL
Scatter panel is illustrative; values shown here are from the notebook's CV and test metrics.
TRUE RUL
PREDICTED
COMPARE AGAINST
Test MAE (early / late): RF 20.54 / 4.02; Elastic Net 25.02 / 20.55; Naive 21.44 / 86.24.
TOP 3 RANDOM FOREST FEATURES
cycle · 0.559
s4_mean · 0.088
s15_mean · 0.048
PHASE 1 / C-MAPSS FD001
09
Notes: Use the predicted-vs-true scatter and the MAE-by-RUL-range bar chart from notebook Section 13. State your actual early and late MAE and explain why they differ in your results.
9

## Slide 10
RUL LAB
09 / TARGET DESIGN
Why the main
model is uncapped
Capping at 125 is a secondary comparison; the project target stays raw RUL.
Same 5-fold CV. Both models are scored against true, uncapped RUL.
TARGET TRANSFORM / SCHEMATIC
RAW RUL
TARGET RUL
cap = 125
Comparison shape only; not a result plot.
5-FOLD GROUPKFOLD / SCORED ON RAW RUL
Capped vs. uncapped
CV RMSE
46.40 ± 2.11
CAPPED
CV MAE
28.90 ± 0.81
CAPPED
CV RMSE
34.78 ± 1.97
UNCAPPED
CV MAE
22.79 ± 0.91
UNCAPPED
FINAL CHOICE + RATIONALE
Keep uncapped. CV RMSE: 34.78 ± 1.97 vs 46.40 ± 2.11; MAE: 22.79 ± 0.91 vs 28.90 ± 0.81. Early MAE: 28.47 ± 1.11 vs 36.55 ± 1.11; late MAE: 5.04 ± 0.34 vs 4.97 ± 0.29 (uncapped vs capped).
Training targets: min(RUL, 125) vs. raw RUL. Score both against uncapped truth to avoid favouring the capped target by construction.
PHASE 1 / C-MAPSS FD001
10
Notes: The brief says cap only if stated. We tested a cap at 125 as a secondary comparison and scored both models on uncapped RUL, the project's target. Scoring a capped model on capped truth would favour it by construction.
10

## Slide 11
RUL LAB
10 / NEXT PHASE
Limits of the
classical baseline
Use the same engine-level split to compare Phase 2 fairly.
01
Fixed settings; no hyperparameter tuning. Window size chosen on the same engines used to compare models.
02
Baseline length (10) and late-life threshold (50) were set by hand, not tested.
03
Two-point slope is simple; one test prediction per engine makes the test score noisy.
04
Only FD001. FD002–FD004 test shifting operating conditions and additional fault modes.
05
Fixed rolling windows may miss longer degradation trends.
PHASE 2 / THE NEXT STEP
From engineered
features to raw
sensor windows
01 Raw sensor windows
02 LSTM sequence model
03 Same engine-level folds
Direct comparison with Phase 1
PHASE 1 / C-MAPSS FD001
11
Notes: Be honest about limits; the viva rewards it. Phase 2 uses the same split so the LSTM is directly comparable.
11

## Slide 12
RUL LAB
12
PHASE 1 COMPLETE
Thank you.
Questions?
PHASE 1 / C-MAPSS FD001
12
Notes: 12